## Slide 1: New Features Added to Our DTI Package
XU, Dongrong Ph.D.
Columbia University
New York State Psychiatric Institute
Support: 1R03EB008235-01A1
June 18, 2009 HBM

## Slide 2
Improvements
Warping Algorithm
Optimized Tensor
Estimation
  Fig. 0. An Overview of the Software Package Dashed lines represent routes of possible data exchange with other available DTI packages. Whereas the functions corresponding to the description are marked in numbers in parenthesis, functions in the 2 color blocks constitute 2 compound tools.

## Slide 3
Seamless Warping of DTI

## Slide 4
Original Fiber
Deformed fiber
Tensors must be reoriented

## Slide 5
Original Fiber
Deformed fiber
Deformed Fiber
Correct
Wrong
Spatial transformation should not be
directly applied to the tensors

## Slide 6
Tensor’s original orientation is important
Shear Force

## Slide 7
Template Space
Original Space
Forward mapping
Backward mapping
Grid locations: no interpolation is needed
Locations where interpolation is required
A potential seam in forward mapping procedures
A location of potential artifact in forward mapping procedures
P1
P2
Forward and Backward Mappings In forward mapping procedures, seams (depicted in the template space with a red cross) will occur when pixels in the original imaging space (black dots) are distributed only to their immediately neighboring grid points in the template space (orange dots). Consequently, artifacts (an example is represented by a blue dot in the figure) will occur at locations of a partial seam (e.g., location P1 generates a seam at the grid point of the blue dot but location P2 does not). In contrast, if backward mapping is used, every discrete location (voxel) in the template space will receive its corresponding value from a point in the original imaging space. However, this description of backward mapping applies only to scalar images. In DTI, backward mapping alone is insufficient because of the additional need to reorient the tensor

## Slide 8: Our New Warping Frame
Issue 4
Issues 1,2,3
+
DTI Normalization
Reorientation by Procrustean Estimation in an optimized neighborhood, based on estimated PDF(•)
Estimate
True
Orientation
PDF Vector
Resample
Procrustean
Estimation
Tensor
Reorientation
Calculate
Correspondence
Bi-directional
Correspondence
(Bijection)
Tensor
Relocation
Estimate
Optimized
Neighborhood

## Slide 9: Seamless DTI Warping
Accuracy Improvement of Realigning Tensor Orientation:
25.96%(within fiber); 9.77%(fiber boundary)
in comparison with the non-seamless DTI Warping
Simulated
Dataset
Real
Dataset
Forward Warping
Seamless Warping

## Slide 10
Optimized Tensor Estimation

## Slide 11
Algorithm
- Smallest combination of DWI along gradient directions with the smallest Condition Number, usually evenly distributed in the 3D space, and optimal J, an index for better image quality re FA & positive definiteness of the tensors
- Expand the combination until the indices become worse

## Slide 12
Figure 2. (a) Correlation of a relative good dataset between individual DWI data and reference baseline data.
Newly Added:
Correlation between DWI & baseline images

## Slide 13
Figure 2. (b) Correlation of a dataset that contain outliers on some image slices.
Slice to be excluded

## Slide 14
A comparison between the results of our method and the manual work of human experts.
No Optimization Our Method Manual Optimization

## Slide 15
Figure 3. Left: DT image without optimization. Middle: Result of our proposed method. Right: Manual result by human technicians.

## Slide 16: Thank you